## Slide 1
Translational Mechanical System
Transfer Functions
There are analogies between electrical and mechanical components and variables.
Mechanical systems, like electrical networks, have three passive, linear components.
  Two of them, the spring and the mass, are energy-storage elements;
  One of them, the viscous damper, dissipates energy.
The two energy-storage elements are analogous to the two electrical energy-storage elements, the inductor and capacitor. The energy dissipator is analogous to electrical resistance.
Mechanical elements are shown in Table 2.4. In the table, K, fv, and M are called spring constant, coefficient of viscous friction, and mass, respectively.

## Slide 2
Translational Mechanical System
Transfer Functions

## Slide 3
Translational Mechanical System
Transfer Functions
Comparing the voltage-current column of Table 2.3 and the force-velocity column of Table2.4 leads that,
  Mechanical force is analogous to electrical voltage,
Also, comparing the voltage-charge column of Table 2.3 and the force-displacement column of Table2.4 leads that,
  Mechanical displacement is analogous to electrical charge,
  The spring is analogous to the capacitor,
  The viscous damper is analogous to the resistor.
Another analogy can be drawn by comparing the force-velocity column of Table 2.4 to the current-voltage column of Table 2.3 in reverse order:
  Mechanical force is analogous to electrical current,
  Mechanical velocity is analogous to electrical voltage,
  The spring is analogous to the inductor,
  The viscous damper is analogous to the capacitor.

## Slide 4
Translational Mechanical System
Transfer Functions
The mechanical system requires just one differential equation, called the equation of motion, to describe it. To obtain the transfer function of a mechanical system;
  We will begin by assuming a positive direction of motion, for example, to the right,
  Using our assumed direction of positive motion, we first draw a free-body diagram (for each mass), placing on the body all forces that act on the body either in the direction of motion or opposite to it,
  Next we use Newton’s law to form a differential equation of motion by summing the forces and setting the sum equal to zero.
  Finally, assuming zero initial conditions, we take the Laplace transform of the differential equation, separate the variables, and arrive at the transfer function.

## Slide 5
EXAMPLE (2.16, pp.63) Transfer function of one equation of motion
Find the transfer function, X(s)/F(s).
The free-body diagram:
Note that,
All the forces felt by the mass are placed on the mass, and we assumed the mass is traveling toward the right.
Thus only the applied force points to the right, and all other forces (the spring, viscous damper and the force due to acceleration) act to oppose it.

## Slide 6
Translational Mechanical System
Transfer Functions
Taking the Laplace transform of the force-displacement column in Table 2.4, we obtain for the spring
for the viscous damper,
and for the mass
If we define impedance for mechanical components as
Replacing each force in Figure 2.16(a) by its Laplace transform,
which is in the format, we obtain
from which we could have obtained

## Slide 7
EXAMPLE (2.17, pp.65) Transfer function of two equation of motion
Find the transfer function, X2(s)/F(s).
The system has two degrees of freedom, since each mass can be moved in the horizontal direction while the other is held still. Thus, two simultaneous equations of motion will be required to describe the system.
The two equations come from free-body diagrams of each mass. Superposition is used to draw the free body diagrams. For example, the forces on M1 are due to (1) its own motion and (2) the motion of M2 transmitted to M1 through the system. We will consider these two sources separately.
If we hold M2 still and move M1 to the right, we see the forces shown below

## Slide 8
EXAMPLE (2.17, pp.65) Transfer function of two equation of motion
If we hold M1 still and move M2 to the right, we see the forces shown below
The total force on M1 is the superposition, or sum, of the forces
If we move M2 to the right while holding M1 still
If we move M1 to the right and hold M2 still

## Slide 9
EXAMPLE (2.17, pp.65) Transfer function of two equation of motion
Then, the total force on M1 is the superposition, or sum, of the forces
The Laplace transform of the equations of motion can now be written
From this, the transfer function, X2(s)=F(s), is

## Slide 10
Rotational Mechanical System Transfer Functions
Rotational mechanical systems are handled the same way as translational mechanical systems, except that torque replaces force and angular displacement replaces translational displacement.
The mechanical components for rotational systems are the same as those for translational systems, except that the components undergo rotation instead of translation.
The table below shows the components along with the relationships between torque and angular velocity, as well as angular displacement.

## Slide 11
Rotational Mechanical System Transfer Functions
Notice that the term associated with the mass is replaced by inertia. The values of K, D and J are called spring constant, coefficient of viscous friction, and moment of inertia, respectively.
Similar to the translational systems, we test a point of motion by rotating it while holding still all other points of motion. The number of points of motion that can be rotated while all others are held still equals the number of equations of motion required to describe the system.
Writing the equations of motion for rotational systems is similar to writing them for translational systems; the only difference is that the free-body diagram consists of torques rather than forces. We obtain these torques using superposition.
  First, we rotate a body while holding all other points still and place on its free-body diagram all torques due to the body’s own motion.
  Then, holding the body still, we rotate adjacent points of motion one at a time and add the torques due to the adjacent motion to the free-body diagram.
  The process is repeated for each point of motion.
  For each free-body diagram, these torques are summed and set equal to zero to form the equations of motion.

## Slide 12
EXAMPLE (2.19, pp.71) Transfer function of two equations of motion
Find the transfer function, θ2(s)/T(s). The rod is supported by bearings at either end and is undergoing torsion. A torque is applied at the left, and the displacement is measured at the right.
There are two degrees of freedom, since each inertia can be rotated while the other is held still. Hence, it will take two simultaneous equations to solve the system.
Now we can draw a free-body diagram of J1, using superposition. The figure below shows the torques on J1 if J2 is held still and J1 rotated.

## Slide 13
EXAMPLE (2.19, pp.71) Transfer function of two equations of motion
The figure below shows the torques on J1 if J1 is held still and J2 rotated.
So, the final (sum) free-body diagram is given below.
Repeating the same process for J2 gives

## Slide 14
EXAMPLE (2.19, pp.71) Transfer function of two equations of motion
Summing torques respectively from free-body diagrams, we obtain the equations of motion,
from which the required transfer function is found to be

## Slide 15
EXAMPLE (2.20, pp.72) Equations of motion by inspection
Write, but do not solve, the Laplace transform of the equations of motion for the system
The equations will take on the following form, similar to electrical mesh equations:

## Slide 16
Transfer Functions for Systems with Gears
Rotational systems, especially those driven by motors, are rarely seen without associated gear trains driving the load. Gears provide mechanical advantage to rotational systems.
Anyone who has ridden a 10-speed bicycle knows the effect of gearing. Going uphill, you shift to provide more torque and less speed. On the straightaway, you shift to obtain more speed and less torque. Thus, gears allow you to match the drive system and the load—a trade-off between speed and torque.
For many applications, gears exhibit backlash, which occurs because of the loose fit between two meshed gears. The drive gear rotates through a small angle before making contact with the meshed gear.
The result is that the angular rotation of the output gear does not occur until a small angular rotation of the input gear has occurred. In this section, we idealize the behavior of gears and assume that there is no backlash.
The linearized interaction between two gears is depicted in the figure.

## Slide 17
Transfer Functions for Systems with Gears
An input gear with radius r1 and N1 teeth is rotated through angle θ1(t) due to a torque, T1(t). An output gear with radius r2 and N2 teeth responds by rotating through angle θ2(t) and delivering a torque, T2(t). From the figure, as the gears turn, the distance traveled along each gear’s circumference is the same. Thus,
If we assume the gears are lossless, that is they do not absorb or store energy, the energy into Gear 1 equals the energy out of Gear 2. Since the translational energy of force times displacement becomes the rotational energy of torque times angular displacement,
Thus, the torques are directly proportional to the ratio of the number of teeth. All results can be summarized in

## Slide 18
Transfer Functions for Systems with Gears
The following figure shows gears driving a rotational inertia, spring, and viscous damper. We want to represent the figure as an equivalent system at θ1 without the gears.
In this system, T1 can be reflected to the output by multiplying by N2=N1.
Now, we can convert θ2(s) into an equivalent θ1(s), so that the previous equation will look as if it were written at the input. Using the first figure (a) to obtain θ2(s) in terms of θ1(s), we get

## Slide 19
Transfer Functions for Systems with Gears
Thus, the load can be thought of as having been reflected from the output to the input.
Generalizing the results, we can make the following statement: Rotational mechanical impedances can be reflected through gear trains by multiplying the mechanical impedance by the ratio
where the impedance to be reflected is attached to the source shaft and is being reflected to the destination shaft.

## Slide 20
EXAMPLE (2.21, pp.76) System with lossless gears
Find the transfer function, θ2(s) /T1(s), for the system
It may be tempting at this point to search for two simultaneous equations corresponding to each inertia. The inertias, however, do not undergo linearly independent motion, since they are tied together by the gears. Thus, there is only one degree of freedom and hence one equation of motion.
We first reflect the impedances (J1 and D1) and torque (T1) on the input shaft to the output where the impedances are reflected by (N2=N1)2 and the torque is reflected by (N2/N1). The equation of motion can now be written as

## Slide 21
EXAMPLE (2.21, pp.76) System with lossless gears
Solving for θ2(s) /T1(s), the transfer function is found to be

## Slide 22
Electromechanical System Transfer Functions
Now, we move to systems that are hybrids of electrical and mechanical variables, the electromechanical systems.
A motor is an electromechanical component that yields a displacement output for a voltage input, that is, a mechanical output generated by an electrical input.
The schematic of an armature-controlled dc servomotor can be derived as
In this schematic,
A magnetic field is developed by stationary permanent magnets or a stationary electromagnet called the fixed field.
A rotating circuit called the armature, through which current ia(t) flows, passes through this magnetic field at right angles and feels a force, F = B l ia(t), where B is the magnetic field strength and l is the length of the conductor.
The resulting torque turns the rotor, the rotating member of the motor.

## Slide 23
Electromechanical System Transfer Functions
A conductor moving at right angles to a magnetic field generates a voltage at the terminals of the conductor equal to e = Blv, where e is the voltage and v is the velocity of the conductor normal to the magnetic field. Since the current-carrying armature is rotating in a magnetic field, its voltage is proportional to speed. Thus,
We call vb(t) the back electromotive force (back emf); Kb is a constant of proportionality called the back emf constant; and dθm(t)/dt = ωm(t) is the angular velocity of the motor. Taking the Laplace transform, we get
The relationship between the armature current, ia(t), the applied armature voltage, ea(t), and the back emf, vb(t), is found by writing a loop equation around the Laplace transformed armature circuit
The torque developed by the motor is proportional to the armature current; thus,

## Slide 24
Electromechanical System Transfer Functions
where Tm is the torque developed by the motor, and Kt is a constant of proportionality, called the motor torque constant, which depends on the motor and magnetic field characteristics. In a consistent set of units, the value of Kt is equal to the value of Kb.
Now we must find Tm(s) in terms of θm(s) if we are to separate the input and output variables and obtain the transfer function, θm(s) /Ea(s).
If we assume that the armature inductance, La is small compared to the armature resistance, Ra, which is usual for a dc motor, Eq. (2.151) becomes