## Slide 1
Prof. Dr. Galip Cansever Altınbaş University Faculty of Engineering and Natural Science, Electrical & Electronics Dept. Mahmutbey Technology Campus (Central Campus) Mahmutbey, Istanbul, Turkey, 34217
Welcome to Dynamic Systems and Control
e-mail: galip.cansever@altinbas.edu.tr T: +90-212-604 01 00/4074

## Slide 2
Instructor: Prof. Dr. Galip Cansever
Grading:
Midterm exam: 1 exam 60%
Final exam: 40%

## Slide 3
Textbooks
N. S. Nise, Control Systems Engineering, 6th edition, John Wiley & Sons, MA, 2011.
G. F. Franklin, J. D. Powell, and A. Emami-Naeini, Feedback Control of Dynamic Systems, 6th edition, Prentice Hall, NJ, 2010
K. Ogata, Modern Control Engineering, 5th edition, Prentice Hall, NJ, 2010
C.L. Phillips, and J. Parr, Feedback Control Systems, 5th Ed., Prentice-Hall, 2010.
F. Golnaraghi and B. C. Kuo, Automatic Control Systems, 9th edition, John Wiley & Sons, NJ, 2010 (This book is available in Turkish by A. Bir, Literatür Yayıncılık)
J. J. D'Azzo, C. H. Houpis, and S. N. Sheldon, Linear Control System Analysis and Design with Matlab, 5th edition, Marcel Dekker, 2003

## Slide 4
  Introduction to Feedback Control System
  Modeling in the Frequency Domain
  Modeling in the Time Domain
  Time Response for First-order & Second-order systems
  Stability
  Feedback and Block Diagrams
  Steady-State Errors
  Root Locus
  Controller Design via Root Locus
Topics

## Slide 5
In this chapter we describe a general process for designing a control system.
A control system consisting of interconnected components is designed to achieve a desired purpose. To understand the purpose of a control system, it is useful to examine examples of control systems through the course of history. These early systems incorporated many of the same ideas of feedback that are in use today.
Modern control engineering practice includes the use of control design strategies for improving manufacturing processes, the efficiency of energy use, advanced automobile control, including rapid transit, among others.
We also discuss the notion of a design gap. The gap exists between the complex physical system under investigation and the model used in the control system synthesis.
The iterative nature of design allows us to handle the design gap effectively while accomplishing necessary tradeoffs in complexity, performance, and cost in order to meet the design specifications.
Chapter 1: Introduction to Control Systems
Objectives

## Slide 6
Control system
An interconnection of components that provide a desired system response
Key enabling technology in all branches of engineering
Used whenever some quantity (e.g., temperature, altitude, speed, concentration, pH) must be made to behave in some desirable way over time
Often exploits feedback to help regulate the system response
What is control? -1

## Slide 7
Control system
Compare actual behavior with desired behavior
Take corrective action based on the difference.
Subsystems and processes (plants) assembles for the purpose of controlling the outputs of the process.
Example: AC, elevator, antenna system, remote controlled robot
Example: student performance
Input = study time, output = grade)
What is control? -2
Notes: A simple idea, but very powerful concept

## Slide 8
Basic Concepts
System – An interconnection of elements and devices for a desired purpose.
Control System – An interconnection of components forming a system configuration that will provide a desired response.
Process – The device, plant, or system under control. The input and output relationship represents the cause-and-effect relationship of the process.

## Slide 9
Open – Loop vs. Closed Loop -1

## Slide 11
Feedback is a central feature of life. The process of feedback governs how we grow, respond to stress and challenge, and regulate factors such as body temperature, blood pressure, and cholesterol level. The mechanisms operate at every level, from the interaction of proteins in cells to the interaction of organisms in complex ecologies.

## Slide 12
A transducer is a device that converts one form of energy to another. Usually a transducer converts a signal in one form of energy to a signal in another.
Transducers are often employed at the boundaries of automation, measurement, and control systems, where electrical signals are converted to and from other physical quantities (energy, force, torque, light, motion, position, etc.). The process of converting one form of energy to another is known as transduction

## Slide 13
Active
Active sensors do not require an external power source to operate, which is called an excitation signal. The signal is modulated by the sensor to produce an output signal. For example, a thermistor does not generate any electrical signal, but by passing an electric current through it, its resistance can be measured by detecting variations in the current and/or voltage across the thermistor, LVDT.
Passive
Passive sensors generate electric signals in response to an external stimulus without the need of an additional energy source. Such examples are a photodiode, and a piezoelectric sensor, thermocouple.

## Slide 14
Bidirectional
Bidirectional transducers convert physical phenomena to electrical signals and also convert electrical signals into physical phenomena. Examples of inherently bidirectional transducers are antennae, which can convert conducted electrical signals to or from propagating electromagnetic waves, and voice coils, which convert electrical signals into sound (when used in a loudspeaker) or sound into electrical signals (when used in a microphone). Likewise, DC electric motors may be used to generate electrical power if the motor shaft is turned by an external torque.[2]
Ideal characteristics
High dynamic range
High repeatability
Low noise
Low hysteresis

## Slide 15
Sensors
A sensor is a device that receives and responds to a signal or stimulus. Transducer is the other term that is sometimes interchangeably used instead of the term sensor, although there are subtle differences. A transducer is a term that can be used for the definition of many devices such as sensors, actuators, or transistors.
Actuators
An actuator is a device that is responsible for moving or controlling a mechanism or system. It is operated by a source of energy, which can be mechanical force, electrical current, hydraulic fluid pressure, or pneumatic pressure, and converts that energy into motion. An actuator is the mechanism by which a control system acts upon an environment. The control system can be simple (a fixed mechanical or electronic system), software-based (e.g. a printer driver, robot control system), a human, or any other input.

## Slide 16
Open – Loop vs Closed Loop -2
O-L | C-L | Description
X |  | Cannot compensate for disturbances that affect the plant
 | X | Higher accuracy and robustness to disturbances
X |  | Commanded by the input
 | X | Commanded by the error via feedback
 | X | Relatively more complex and expensive
 | X | Improved performance and stability

## Slide 17
Two main types of control
Multivariable Control System
Open-Loop Control Systems utilize a controller or control actuator to obtain the desired response.
Closed-Loop Control Systems utilizes feedback to compare the actual output to the desired output response.

## Slide 18
History
18th Century James Watt’s centrifugal governor for the speed control of a steam engine.
1920s Minorsky worked on automatic controllers for steering ships.
1930s Nyquist developed a method for analyzing the stability of controlled systems
1940s Frequency response methods made it possible to design linear closed-loop control systems
1950s Root-locus method due to Evans was fully developed
1960s State space methods, optimal control, adaptive control and
1980s Learning controls are begun to investigated and developed.
Present and on-going research fields. Recent application of modern control theory includes such non-engineering systems such as biological, biomedical, economic and socio-economic systems

## Slide 19
(a) Automobile steering control system.
(b) The driver uses the difference between the actual and the desired direction of travel
to generate a controlled adjustment of the steering wheel.
(c) Typical direction-of-travel response.
Examples of Modern Control Systems

## Slide 20
Examples of Modern Control Systems

## Slide 21
Examples of Modern Control Systems

## Slide 22
The Future of Control Systems

## Slide 23
Control System Design

## Slide 24
Antenna Azimuth Position Control

## Slide 25
Design Stages for the Antenna

## Slide 28
Step-3: Draw Schematic

## Slide 29
Step-4: Draw Block Diagram

## Slide 30
Design Example

## Slide 31
Design Example

## Slide 32
Example: Elevator Control
Consider an elevator.
When the 4th floor button is pressed on the 1st floor, the elevator rises,
The speed and the floor leveling accuracy are designed for passenger comfort,
The performance of the elevator can be seen from the elevator response curve below

## Slide 33
Transient and steady state response of an elevator
There are two major measures of performance are apparent,
  transient response,
  steady-state error.
If transient response is too fast, passenger comfort is sacrificed,
If it is too slow, passenger patience is sacrificed.
On the other hand, if the elevator did not properly level, then passenger safety and convenience would be sacrificed.

## Slide 34
Three terms needed to know
Transient response
Steady-state response
Stability: most important thing in analysis and design objectives

## Slide 35
Analysis and Design Objectives
• Transient Response must meet certain criteria.
  Mainly: Speed and max. overshoot.
• Steady-State Response must meet certain criteria.
  Mainly: small or zero error
• The system must have Stability.
  Total Response = Natural Response + Forced Response
    Natural response describes the way the system dissipates or gain energy. It is dependent only on the system not the input
    Forced response depends on the input.
    Natural response must go to zero leaving only the forced response or oscillate

## Slide 36
  In electrical engineering and mechanical engineering, a transient response or natural response is the response of a system to a change from an equilibrium or a steady state. The transient response is not necessarily tied to "on/off" events but to any event that affects the equilibrium of the system. The impulse response and step response are transient responses to a specific input (an impulse and a step, respectively).

## Slide 37
Rise time
  Rise time refers to the time required for a signal to change from a specified low value
  to a specified high value. Typically, these values are 10% and 90% of the step height.
Overshoot
  Overshoot is when a signal or function exceeds its target. It is often associated with ringing.
Settling time
  Settling time is the time elapsed from the application of an ideal instantaneous step
  input to the time at which the output has entered and remained within a specified .
Delay-time
  The delay time is the time required for the response to reach half the final value the
  very first time.[1]
Peak time
  The peak time is the time required for the response to reach the first peak of the overshoot.[1]
Steady-state error
  2003's Instrument Engineers' Handbook defines the steady-state error of a system as
  "the difference between the desired final output and the actual one" when the system
  reaches a steady state, when its behavior may be expected to continue if the system is undisturbed.[2]