## Slide 1: Food Processing Machine and Equipment Cleaning and Sorting
Dr. Salih KARASU

## Slide 2: Pretreatment proces
The raw materials represent a major cost factor. Hence, it is very important to procure the raw materials that comply with the specifications laid down by the manufacturer of the plant so as to minimize the defect levels
The selection of raw materials as well as selection of preparatory operations should be done in such a way so as to minimize the waste and to maximize the product yield.

## Slide 3
Cleaning
All raw materials must be subjected to cleaning process before production. The main reason for the cleaning process;
To protect consumer health,
To increase the quality of raw materials and to ensure the good quality of the final products
Prevent food equipment from being damaged
Prevent product loss

## Slide 4
All materils with exception of high quality raw material can be defined as foreign material

## Slide 5: Impurities for food industry
impurities | Exp.
Metals | Iron, copper, aluminum…
Petroleum products and minerals | Soil, stone, motor oils, diesel
Plant origin | Leaf, straw, stalk, seed, ...
Origin of animal | Hair, bone, bug,
Chemicals | Fertilizer, pesticide,
Microorganims | Bacteria, mold, yeast
Microbial metabolites | Microbial toxins, antibiotics,

## Slide 6: Cleaning Methods
The selection of a cleaning method is determined by,
the nature of the product to be cleaned,
the types of contaminant to be removed and,
the desired condition of the cleaned material.
There are basically two types of cleaning methods, which are generally used either singly or in combination- dry cleaning and wet cleaning.

## Slide 7
Different principles are used to remove impurities in differentraw materials.
Fruits and vegetables are subjected to wet cleaning process. Brush, roller and spray systems are used.
The cereals and oily seed are cleaned with pneumatic systems, sieves and metal holders.
The lower dimension impurities are removed with special systems(Ultraviole, X-ray, NMR, sonication)

## Slide 8: Dry cleaning
Dry cleaning methods are used for products that are smaller, have greater mechanical strength and possess lower moisture content.
The main advantages of dry cleaning methods are that, these methods are generally inexpensive and involve cheaper equipment than wet cleaning methods, and produce a concentrated dry effluent which may be disposed of more cheaply,
but it suffers from various disadvantages such as, it is prone to production of dust, which can be a source of product recontamination and in some cases, a fire and explosion hazard.

## Slide 9: Dry cleaning systems
The main groups of equipment used for dry cleaning are:
Aspirators,
Magnetic separators,
Separators based on screening of foods

## Slide 10: Screens
Screens remove contaminants that have sizes different from the product.
A screen in a frame is the simplest form used which has now been largely replaced by continuous types,
such as centrifugal screens,
vibrate,
and the flat bed screens.

## Slide 14
1) Feed 2) Air 3) Internal cylinder 4) Outer cylinder 5) Motor A) Final product B) Impurities

## Slide 18: Air separators
This method is used for the cleaning of grains and oily seed
Forced air separators or aspirators use large quantities of low-pressure air and consume considerable energy.
Control of dust is necessary for safety and health reasons and to prevent the spread of contaminants.
This method should not be used for products, which are sensitive to oxidation.

## Slide 20: Manyetik temizleme
Magnetic cleaning is generally used to remove magnetic contaminants that can damage preparatory equipment from the raw materials.
Rotating or stationary magnetic drums, magnetic belts, magnets located over belts carrying the food, through which the food is passed, are used involving permanent and electromagnets.
The contaminants that adhere to the magnets should be frequently removed to prevent a buildup that can be swept into the product stream, which results in a gross localized recontamination.

## Slide 22
Self cleaning rotary magnets
Seed inlet
aspirator
Rotating drum
Stationary magnet
İron parts
Cleaned seed

## Slide 24: Electrostatic systems
This system is used to clean foods that have the same size and shape characteristics and different surface loads.
This is suitable for grains and oil seeds

## Slide 26: Wet cleaning
Wet cleaning is more effective than dry cleaning for removing soil from root crops or dust and pesticide residues from soft fruits or vegetables. It is also dustless and causes less damage to foods than dry methods. Different combinations of detergents and sterilizers at different temperatures allow flexibility in operation.

## Slide 27: Wet cleaning
Use of warm cleaning water may accelerate chemical and microbiological spoilage unless careful monitoring is done over washing times and subsequent delays before processing.

## Slide 28: Wet Cleaning
The main disadvantage of these methods is that these methods produce large volumes of effluent which have high concentrations of biological oxidation demand (BOD) and chemical oxidation demand (COD). Hence, this requires an additional effluent disposal cost.
To reduce costs, recirculated, filtered and chlorinated water is used whenever possible.

## Slide 29: Wet Cleaning
Examples of wet cleaning equipment,
include- spray washers,
brush washers,
ultrasonic cleaners and,
flotation tanks

## Slide 30
Soaking is the simplest wet cleaning method. It is often used as preliminary stage in the cleaning of root vegetables heavily contaminated with adhering soil.
The soil is softened and partly removed along with stones, sand and other abrasive materials that could damage the machinery used in subsequent cleaning or preparation.
The efficiency of soaking is improved by agitating the raw material to be cleaned by means of propeller- stirrers built into the tank. Alternatively, raw material is fed into a rotating horizontal perforated drum partially submerged in a water tank.
Soaking

## Slide 31: Soaking
The use of warm water and detergents increase the efficiency but the use of chemicals may affect the texture of the food, e.g. sodium hexametaphosphate softens peas while some metal ions toughen peas and peaches destined for canning.
Chlorination is used to decrease bacterial load of water in the soak tank. High levels of chlorine affect the food, e.g. potatoes develop blackened flesh.

## Slide 32: Spray cleaning
Spray washing is one of the most widely used methods for wet cleaning of fruits and vegetables. The surface of the food is subjected to water sprays.
The efficiency of spray washing depends on several parameters such as water pressure, volume of water, temperature, the distance of the foods from jets, the time of spraying and the number of spray jets used.
A small volume of water at high pressure is the most effective combination.
This method may have a disadvantage in case of ripe fruits such as strawberries and tomatoes, which may get damaged during this process.