## Slide 1: Size reduction

## Slide 2: Introduction
In the food industry, raw materials and intermediate products must often be submitted to size reduction operations such as cutting , chopping , grinding , milling and so on.
In the case of liquids and semi-solids, size reduction operations include mashing , atomizing , homogenizing etc.

## Slide 3
The following are some important applications of size reduction in the food industry:
Milling of cereal grains to obtain flour
Fine grinding (refining) of chocolate mass
Flaking of soybeans prior to solvent extraction
Cutting of vegetables and fruits to desired shapes (cubes, strips, slices…)
Fine mashing of baby food
Homogenization of milk and cream.

## Slide 4
Size reduction is a widespread, multipurpose operation. Its may serve a number of different objectives, such as:
Accelerating heat and mass transfer (flaking of soybeans or grinding coffee in preparation to extraction, atomization of milk as a fi ne spray into hot air in spray-drying).
Facilitating separation of different parts of a material (milling wheat to obtain flour and bran separately, filleting of fish).
Obtaining a desirable product texture (refining of chocolate mass, meat grinding).

## Slide 5
Facilitating mixing and dispersion (milling or crushing ingredients for drymixing, homogenization of liquids to obtain stable emulsions)
Portion control (slicing cold-cuts, bread, cakes)
Obtaining pieces and particles of defi ned shapes (cubing meat for stew, cutting pineapple to obtain the familiar wheel-shaped slices, cutting dough to make cookies).

## Slide 6: Size Reduction of Solids, Basic Principles
Mechanism of size reduction in solids
Compression and shear are the two types of force involved in size reduction of solids.
Impact , sometimes given as a third type is, in fact, strong compression applied for a very short time. When such forces act on a solid particle, elastic or plastic deformation occurs, depending on the material.
As the deformation reaches a certain limit value determined by the nature and structure of the solid ( mechanical strength ), the particle breaks along certain planes ( planes of failure ).
In any size reduction operation, all the types of force are usually involved, to different extent.

## Slide 7: Size Reduction of Solids, Equipment and Methods
Impact mills
The principal representative of this class is the hammer mill
The crushing elements are hammers fi tted on a high-speed rotor inside a cylindrical chamber.
The chamber walls may be smooth or lined with corrugated breaker plates.

## Slide 8: Hammer mills
The hammers may be fixed or swinging. Swinging hammers are used when it is necessary to reduce the risk of damage in the case of encounter between the hammer and large, hard chunks.
The principal crushing action takes place as a result of the collision between the particles and the hammers and chamber walls

## Slide 9: Hammer Mills

## Slide 10: Hammer Mills

## Slide 11: Pressure mills
One of the most widespread types of this family is the roller mill,
The material is compressed between a pair of counter-rotating heavy rollers with hardened surfaces to the point of fracture.
The mill may consist of several rollers with gradually decreasing clearance between the rollers.
Roller mills are extensively used in the grain milling industry. Mills equipped with corrugated rollers are used in the initial stages of wheat milling. They are called ‘ breaks’ because they serve to ‘ break ’ the grain and to separate the feed into the main fractions

## Slide 12: Roller mills
Breakers are also used in the dry milling of corn and for fracturing soybeans prior to flaking for the production of oil.
In wheat flour mills, units with smooth rollers are used as the further step of size reduction and are called ‘ refiners ’ as they serve to refine further the fractions to produce the different flours and other products.
Mills consisting of a series of smooth rollers are standard equipment for refi ning chocolate mass.

## Slide 14: Roller Mills

## Slide 15: Roller Mills

## Slide 16: Valsli Değirmen

## Slide 17: Valsli Değirmen
Bir dizi valsli değirmen

## Slide 18
Reduction System
Break System

## Slide 20: Grinding
Pasajlarda kırma ve inceltme işlemlerinde 4 farklı ürün elde edilmektedir;
  Endospermin yapışık olduğu iri kabuk parçaları
  İri endosperm parçaları (irmik)
  İnce endosperm parçaları (dunst)
  En ince endosperm parçaları (un, 1-150).

## Slide 21: Attrition mills
This is a very large group of mills. In many of the types belonging to this class, the material is ground between two corrugated surfaces moving with respect to each other.
The prehistoric stone mill and the familiar household coffee grinder are examples of this kind. Usually one of the surfaces rotates and the other is stationary.
Mills with circular grinding surfaces are also known as disc mills

## Slide 22: Attrition mills
The grinding surfaces may be made of hardened metal or of coarse corundum. Corundum mills are used for reducing the size of particles in suspension down to colloidal range (micrometer range) and are therefore named colloid mills.
They are used in the preparation of fine suspensions such as homogenized strained infant food, comminuted fruit pastes and mustard.

## Slide 23: Attrition mills
The main mechanism of action in attrition mills is shear, due to friction between the particle and the pair of grinding surfaces.
Unless the mill is cooled, the temperature rise may be considerable, particularly in the case of dry milling. A different kind of attrition mill makes use of free ‘ grinding media ’ instead of fixed grinding surfaces.

## Slide 24: Ball Mill
One of the representatives of this kind is the ball mill whereby the feed is vigorously mixed in a vessel containing free spherical bodies (balls) made of materials with different degrees of hardness, from plastic to metal, according to the hardness of the material.
Dry ball-milling is used for fi ne grinding of pigments. Wet ball-milling is one of the methods used for the disintegration of cells in suspension .

## Slide 25: Ball mills
.

## Slide 26: Cutters and choppers
Cutting and chopping are size reduction operations based on shearing through the use of sharp-edged moving elements (knives, blades).
The term ‘ cutting ’ is usually reserved for operations resulting in particles with fairly regular geometric forms (cubes, juliennes, slices), while the term ‘ chopping ’ is applied mainly to random cutting.
The variety of cutting machines used in the food industry is vast.

## Slide 27
The silent cutter is widely used in the meat industry for simultaneous chopping and mixing. A batch of the material to be processed is placed in a horizontal revolving dish. The dish circulated the material through a set of horizontal revolving knives.
Another related type of machine is the bowl mixer cutter

## Slide 28: Cutter