## Slide 2
Answer (Q1):
b)
c) 1 m3 SSD aggregate 1600 kg. In order to obtain 1600 kg SSD aggregate, we should consider the moist content of the aggregates  From 1m3 moist aggregates (1200 kg) we can obtain SSD aggregate. How much more aggregate is needed?
1600 (required)- 1154 (exist)= 446 kg (need) SSD aggregates that we need to obtain 1600 kg SSD agg.
more moist aggregates !!!
Thus, 1200+464=1664 kg moist aggregates needed to obtain 1600 kg SSD aggregates (As mass)
As volume 1664/1200= 1.39 m3 moist aggregate required!!!
d) 1664-1600= 64 kg excess water