## Slide 1: INSPIRE
European Directive 2007/2/EC is known as 'INSPIRE'. INSPIRE establishes an infrastructure for spatial information in the European Union.
The aim of INSPIRE is to facilitate better environmental policy across the EU. This will be chieved by:
improving the joining up of and access to existing spatial data across the European Union at a local, regional, national and international level;
facilitating improvements in the sharing of spatial data between public authorities;
and improving public access to spatial data.
http://data.gov.uk/location/inspire adresinden alınmıştır.

## Slide 2: INSPIRE
What is the INSPIRE Directive?
The INSPIRE directive came into force on 15 May 2007 and will be implemented in various stages, with full implementation required by 2019.
The INSPIRE directive aims to create a European Union (EU) spatial data infrastructure. This will enable the sharing of environmental spatial information among public sector organisations and better facilitate public access to spatial information across Europe.
A European Spatial Data Infrastructure will assist in policy-making across boundaries. Therefore the spatial information considered under the directive is extensive and includes a great variety of topical and technical themes.
INSPIRE is based on a number of common principles:
Data should be collected only once and kept where it can be maintained most effectively.
It should be possible to combine seamless spatial information from different sources across Europe and share it with many users and applications.
It should be possible for information collected at one level/scale to be shared with all levels/scales; detailed for thorough investigations, general for strategic purposes.
Geographic information needed for good governance at all levels should be readily and transparently available.
Easy to find what geographic information is available, how it can be used to meet a particular need, and under which conditions it can be acquired and used.
http://inspire.jrc.ec.europa.eu adresinden alınmıştır.

## Slide 3: INSPIRE
Under INSPIRE Member States must make available in a consistent format spatial datasets which come within the scope of the Directive and also create network services for accessing the datasets. Datasets in scope of INSPIRE are ones which come under one or more of the 34 environmental themes set out in the Directive Annexes.
http://inspire.jrc.ec.europa.eu/index.cfm/pageid/2/list/7

## Slide 4: INSPIRE - cadastral parcel
The INSPIRE Directive focuses on the geographical part of cadastral data. In the INSPIRE context, cadastral parcels will be mainly used as locators for geo-information in general, including environmental data.
Cadastral parcels are considered in the INSPIRE scope if they are available as vector data.
Rights and owners are out of the INSPIRE scope.
Buildings, land use, addresses are considered in other INSPIRE themes.
The current version of ISO 19152 Land Administration Domain Model (LADM) and of the INSPIRE cadastral parcels model are compatible. The LADM provides a wider context for the INSPIRE cadastral parcels. It includes other spatial object types, such as rights and ownership, which are outside the direct scope of INSPIRE.

## Slide 5: INSPIRE - cadastral parcel

## Slide 6: INSPIRE - cadastral parcel
Feature type CadastralParcel (core):
Cadastral parcels are defined by the INSPIRE Directive as “areas defined by cadastral registers or equivalent”. As much as possible, in the INSPIRE context, cadastral parcels should be forming a partition of national territory. Cadastral parcel should be considered as a single area of Earth surface (land and/or water), under homogeneous real property rights and unique ownership, real property rights and ownership being defined by national law.
Cadastral parcels have the following additional attributes:
− a geometry
− a national cadastral reference
− an area value
− portrayal attributes: reference point and label

## Slide 7: INSPIRE - cadastral parcel
Feature type CadastralParcel (core):
Cadastral parcels are considered as under the INSPIRE scope if:
− they fit with the definition given by the Directive “areas defined in cadastral registers or equivalent”
− they fit as much as possible with the description given in this document “single area on Earth surface under homogeneous real property rights and unique ownership, forming a partition of national territory”
− they are available as vector data.

## Slide 8: INSPIRE - cadastral parcel
Feature type CadastralParcel (core):
EXAMPLE 1: France
In France, there are two kinds of “areas defined in cadastral registers or equivalent”:
− parcels (single areas on Earth surface under unique or homogeneous property right)
− sub-parcels (division of parcels based on official land use for taxation purposes)
Only the first one “parcels” have to be published for INSPIRE.
EXAMPLE 2: Finland
In Finland, basic units "in cadastral registers or equivalent" are called basic property units. Areas of basic property units are called parcels. Notice: in Finland, one basic property unit can be composed from 0 to many parcels. The parcels will be published for INSPIRE as cadastral parcels. Basic property units composed of 1 to many parcels may also be published for INSPIRE.

## Slide 9: INSPIRE - cadastral parcel
Feature type CadastralZoning (auxiliary):
Cadastral zonings are the intermediary areas (such as municipalities, sections, blocks, …) used in order to divide national territory into cadastral parcels.
Cadastral zonings have the following additional attributes:
− a geometry
− a national cadastral zoning reference
− a name, if any
− a level in the national cadastral hierarchy and the name of this level
− portrayal attributes : reference point and label
− metadata attributes : original map scale denominator and estimated accuracy

## Slide 10: INSPIRE - cadastral parcel
Feature type CadastralBoundary (auxiliary):
In the INSPIRE context, cadastral boundaries are to be made available by Member States where absolute positional accuracy information is recorded for the cadastral boundary.
Cadastral boundaries have the following additional attributes:
- a geometry
- metadata attribute: estimated accuracy

## Slide 11: INSPIRE - cadastral parcel
Feature type BasicPropertyUnit (auxiliary)
Basic property units are the basic units of ownership that are recorded in the land books, land registers or equivalent. They are defined by unique ownership and homogeneous real property rights, and may consist of one or more adjacent or geographically separate parcels. In the INSPIRE context, basic property units are to be used by countries where unique cadastral references are given only for basic property units and not for parcels. Basic Property units allow these countries to provide information about area or about temporal validity in the cadastral register. Basic property units have the following additional attributes:
a national cadastral reference
an area value
In countries as Norway and Finland the basic unit
in registration is basic property unit

## Slide 12: INSPIRE cadastral parcel and LADM
INSPIRE cadastral parcels model can be derived from the LADM. In INSPIRE context four classes are relevant:
− LA_Parcel as basis for CadastralParcel,
− LA_LAUnit as basis for BasicPropertyUnit,
− LA_FaceString as basis for CadastralBoundary,
− LA_SpatialUnitSet as basis for CadastralZoning.
The LADM attributes inherited by INSPIRE can have a more specific data type or cardinality in
INSPIRE (compared to LADM).

## Slide 13: INSPIRE cadastral parcel and LADM

## Slide 14: INSPIRE cadastral parcel and LADM
nationalCadastralReference
Every country has different cadastral references with different structure, which carries different meanings: sometimes a hierarchical cadastral division is stored in the cadastral reference, sometimes some lineage can be observed etc…
EXAMPLES
Austria: 30133-123/45, behind the / is the result of dividing an (earlier) parcel
Belgium: 92001A0999_02R999, cadastral division key (5d), section (1l), root (4d), bis (‘_’+2d), alphanumeric (1l or ‘ ’), numeric (3d)
Denmark: 590151,157h, cadastral district (max 7d), parcel id (max 4d+3L)
Finland: 09140300020017, municipality number (3d), cadastral division number (3d), group number (4d) and sequence number (4d)
Spain: two options:
urban: 9872023 VH5797S 0001 WX, estate/parcel (7d), sheet (7c), flat/unit (4d), control (2l)
rural: 13 077 A 018 00039 0000 FP, province (2d), municipality (3d), sector (1l), polygon (3d), parcel (5d), sub-parcel (4d), control (2l)
The Netherlands: APD00 F 2345, municipality (3l+2d), section (2l), parcel (5d)
− ....

## Slide 15: INSPIRE - Building
The normative core profile contain feature types building and building part and a limited set of attributes mainly related to temporal aspects (construction, renovation and demolition dates), physical information (height, number of floors, elevation) and the classification of buildings according to their physical aspect and current use. Core profile includes two schemas for different geometries:
The Buildings2D profile includes various geometrical representations of buildings as 2D data. The Buildings3D profile has same semantic content as the Buildings2D profile and allows the geometric representation of buildings in 3D.
The extended profiles contain the recommendations to provide more detailed information about buildings. In addition to building and building part, the main features represented are other constructions, building units and installations. The informative extended profile includes two schemas for different geometries:
The BuildingsExtended2D profile is a semantic extension of Buildings2D with additional thematic attributes (material of construction, official area or value, connection to utility networks…), classes (building units, installations, other constructions) and references to other data (like cadastral data and addresses). The BuildingsExtended3D profile is an extension of the Buildings3D profile for rich 3D representations at different levels of details. It includes many building components, such as the building boundaries (wall, roof …), the openings (doors – windows) and building interior (rooms, internal installations) and the textures.

## Slide 17
Base (core) application schema includes 2 abstract feature types:
AbstractConstruction is an abstract feature type grouping the semantic properties of buildings, building parts and of some optional feature types that may be added to core profiles, in order to provide more information about theme Buildings. The optional feature types are described in extended application schemas.
AbstractBuilding is an abstract feature type grouping the common properties of instanciable feature types Building and BuildingPart

## Slide 18: INSPIRE - Building
Buildings are enclosed constructions above and/or underground which are intended or used for the shelter of humans, animals, things or the production of economic goods and that refer to any structure permanently constructed or erected on its site.
According to a a CityGML concept, a complex building may be considered as an aggregation of BuildingParts.
A BuildingPart is a sub-division of a Building that might have been considered as a building and that is homogeneous related to its physical, functional or temporal aspects.
It is up to each data producer to define what is considered as a Building and what is considered as a BuildingPart (if this concept is used)

## Slide 19
A building or a construction may have several values of attribute elevation:
the elevation may be measured at different levels of the building; this must be documented with attribute elevationReference, using the possible values given in the code list ElevationReferenceValue
the elevation may be given in various vertical reference systems; this has to be documented through the DirectPosition that contains both the elevation value itself and the Coordinate Reference System to which this value refers.

## Slide 20
A construction of a building may have several values for the attribute heightAboveGround, according to the levels that were chosen to compute it.
The HeightAboveGround of a construction or building is generally computed as the difference between an elevation measured at a high reference and the elevation measured at a low reference.

## Slide 21
Attribute externalReference
This attribute aims to ensure the link to other information systems, for instance:
another spatial data set including building data; in this case, the external reference contributes to ensure consistency between different views or different levels of detail on same real-world objects, that is an explicit requirement of the INSPIRE Directive
the cadastral register where information about owner, tenant, criteria of valuation (heating, toilet, …) may be found.

## Slide 22
Classification of buildings
The classification of buildings has to be done using two attributes:
the attribute currentUse that focuses on the activity hosted by the building; this attribute aims to fulfil management requirements, such as computation of population or spatial planning ; this classification aims to be exhaustive for the functional buildings hosting human activities
the attribute buildingNature that focuses on the physical aspect of the building; however, this physical aspect is often expressed as a function (e.g. stadium, silo, windmill); this attribute aims to fulfil mainly mapping purposes and addresses only specific, noticeable buildings. This is a rather short and simple list of possible values, with focus on two international use cases: air flights where buildings may be obstacles and marine navigation where buildings may be landmarks

## Slide 23
The code list for attribute currentUse may also be extended by Member States, but only by providing more detailed values, under the hierarchical structure of the INSPIRE code list.

## Slide 25: INSPIRE - Building
A BuildingPart is a sub-division of a Building that is homogeneous related to its physical, functional or temporal aspects. It is up to each data producer to define what is considered as a Building and what is considered as a BuildingPart (if this concept is used). This information has to be provided as metadata. Buildings and BuildingParts share the same set of properties that are factorised in the feature type AbstractBuilding.

## Slide 26
2D data: geometry of features is represented in a two-dimensional space. In other words, the geometry of 2D data is given using (X,Y) coordinates.
2.5D data: geometry of features is represented in a three-dimensional space with the constraint that, for each (X,Y) position, there is only one Z.
3D data: geometry of features is represented in a three-dimensional space. In other words, the geometry of 2D data is given using (X,Y,Z) coordinates without any constraints.

## Slide 27: INSPIRE - Building
The INSPIRE model is quite flexible as it allows the geometry of a building to be represented in different ways.

## Slide 28: INSPIRE - Building
A building is a 3D object represented in this profile by 2D or 2,5 D data:
− the place where (X,Y) coordinates were captured has to be documented using the attribute horizontalGeometryReference;
− the place where Z coordinate was captured must be documented by attribute VerticalGeometryReference.

## Slide 29
The Buildings 2D application schema inherits of the semantics of Buildings base application schema and defines the geometric representation of buildings and building parts, using the data type BuildingGeometry2D, also defined in the Buildings Base application schema.

## Slide 30
The Buildings 3D application schema inherits of the semantics of Buildings base application schema and defines the geometric representation of buildings and building parts:
The 3D representation has to be provided, using any of the LoD of City GML
A 2D (or 2,5D) representation is allowed by the voidable attribute geometry2D

## Slide 31
Buildings and building parts may be represented using any of the four levels of detail of City GML:
in LoD1 (block model), a Building (or BuildingPart) is represented in a generalized way as right prism with vertical walls and horizontal ‘roofs’. In LoD2, a Building or BuildingPart is represented by a generalised way with vertical lateral surfaces and a prototypical roof or cover shape
InLod3 and LoD4, a Building or BuildingPart is represented by its real detailed shape for lateral faces (including protrusions, facade elements, and window recesses) as well as of the roof (including dormers, chimneys)

## Slide 32
This means that it is possible, for instance:
to choose one LoD and to use it for all buildings in the data set
to use, in same data set, LoD1 for some buildings, LoD2 for some others and LoD3 or LoD4 for the last ones.
To have, in same data set, several representations for the same building (e.g. one in LoD2 and one in LoD3)
Typically, in many existing data, ordinary buildings are represented using LoD1 or LoD2 whereas noticeable buildings or buildings in a project area will be represented with more details (LoD2, LoD3 or
even LoD4).

## Slide 33
Buildings Base Extended is an abstract application schema describing the additional semantics that is
common to instanciable application schemas Buildings Extended2D and Buildings Extended3D.

## Slide 34
Buildings Base Extended contains mainly 3 new feature types:
OtherConstructions are self-standing constructions that are generally not considered as buildings. This extended profile includes the most significant constructions that are necessary to describe landscape and to fulfil use cases such as safety or spatial planning.
Installations are constructions, generally of small size that are attached to a Building (or a BuildingPart).
BuildingUnits are subdivisions of Building with their own lockable access from the outside or from a common area (i.e. not from another BuildingUnit), which are atomic, functionally independent, and may be separately sold, rented out, inherited, etc.

## Slide 35
Other constructions inherit of the attributes of AbstractConstruction (from <BuildingsBase> ) and are mainly described by their nature, that may take following values:

## Slide 36
Installations inherit of the attributes of AbstractConstruction (from <BuildingsBase> ) and are mainly described by their nature, that may take the following values.

## Slide 37
New properties
The additional properties that are common to buildings, building parts and building units are grouped in feature type BuildingAndBuildingUnitInfo. These common attributes are mainly related to official information. In addition to the common attributes, BuildingAndBuildingUnitInfo has associations to feature types Address and Cadastral Parcels that are in annex I themes.

## Slide 38
New properties
The additional properties that are specific to buildings and building parts are grouped in feature type BuildingInfo. These attributes address the physical description with more details than in the <Buildings Base> application schema.

## Slide 43
New properties
Attribute Document
The INSPIRE model allows the possibility to link documents to a building or a building part or a floor or a building unit; various documents may be concerned, such as images, sketches, building permits, emergency plans. The attribute Document is defined as a data type with the link to the place the document may be found and with a simple set of metadata elements.

## Slide 44
New properties
Attribute officialValue
The attribute official value may be submitted to access restrictions due for instance to privacy issues. Consequently, the INSPIRE model allows this information to be provided, either directly by its value and currency or indirectly by the external reference to another information system. In first case, the access to the information of official area is widely open, following INSPIRE rules. In the second case, the access to the other external information system may be restricted to authorized users. In addition to the official value itself, some metadata elements should be provided in order to indicate what the official value represents.

## Slide 45
The GeoNames contains over 10 million geographical names and consists of over 9 million unique features whereof 2.8 million populated places and 5.5 million alternate names. All features are categorized into one out of nine feature classes and further subcategorized into one out of 645 feature codes. The data is accessible free of charge through a number of webservices and a daily database export. GeoNames is already serving up to over 150 million web service requests per day. GeoNames is integrating geographical data such as names of places in various languages, elevation, population and others from various sources. All lat/long coordinates are in WGS84 (World Geodetic System 1984). Users may manually edit, correct and add new names using a user friendly wiki interface.
http://www.geonames.org

## Slide 46
Ülkemizde yer adları dizini kapsamında, Harita Genel Komutanlığı (HGK) tarafından 1/250.000 Ölçekli Türkiye ve Çevresi Coğrafi Ad Dizini ile Türkiye Yerleşim Yerleri Veri Tabanı geliştirilmiştir.
1/250.000 Ölçekli Türkiye ve Çevresi Coğrafi Ad Dizini, Türkiye ve çevresine ait yerleşim yerleri, topografik ve hidrografik detayların; adları, türleri ve coğrafi koordinatlarını basılı formatta sunmaktadır.
Türkiye Yerleşim Yerleri Veri Tabanı ise yerleşim yerlerinin ID numarası, resmi yer adı, 1/25.000 ölçekli paftası ve grid numaraları, coğrafi koordinatları ve yüksekliğine ilişkin verileri içermektedir.
İçişleri Bakanlığı da idari birimlerin basit bir listesini sunan Mülki İdare Birimleri Envanterini oluşturmuştur. Bu envanter; idari birim adlarını basit bir liste biçiminde sunmakta, Web ara yüzü ile sorgulanan birimin bağlı olduğu birim adını ve türünü göstermektedir.

## Slide 47
http://araziyonetimi.org/
Abdullah Kara, YL tezi

## Slide 48: Adres ve Numaralamaya İlişkin Yönetmelik
Bu Yönetmeliğin amacı, binaların numaralandırılması, numaralandırılan binalara ait adreslerin Ulusal Adres Veri Tabanına işlenmesine ilişkin usul ve esasları belirlemektir.
Ulusal adres veri tabani: Türkiye Cumhuriyeti sınırları içinde adres bileşenleri ile tanımlanmış tüm adreslerin tutulduğu merkezi veri tabanıdır.
Adres: Herhangi bir toprak parçası veya binanın coğrafi konumu ve işlevi açısından tanımlanması,
Bina: Kendi başına kullanılabilen bir veya birden fazla konut ya da işyeri birimini kapsayan, bir tavan veya çatı ile örtülmüş, temelden tavana kadar uzanan dış duvarlar ile kaplanmış, üstü örtülü ve insanların oturma, çalışma, eğlenme, dinlenme veya ibadet etmelerine imkan sağlayan, hayvanların ve eşyaların korunmasına yarayan, sanayi, ticaret, eğitim ve diğer kullanımlar için tasarlanmış yapıları,
Adres standardı; il, ilçe, bucak, köy, mezra, belediye adı, mahalle adı ve tanıtım numarası, meydan, bulvar, cadde, sokak ve küme evlerin adı ve tanıtım numarası ile site adı, blok adı, mevki adı, dış kapı numarası, iç kapı numarası ve posta kodu bileşenlerinden oluşur. Bu bileşenlerden il adı, ilçe adı, dış kapı numarası ve posta kodunun her adreste bulunması zorunludur.

## Slide 49: Adres ve Numaralamaya İlişkin Yönetmelik
Adres bileşenleri
İl: Merkezi idarenin taşra birimlerinin en büyüğüdür.
İlçe: İdari bakımından mülki taksimatta ilden sonra gelen yerleşim birimidir.
Köy: Mahalli idare teşkilatının en küçük yerleşim yeridir.
Mahalle: Belediye sınırları içinde, ihtiyaç ve öncelikleri benzer özellikler gösteren ve sakinleri arasında komşuluk ilişkisi bulunan idari birimdir.
Bulvar: Yerleşim yeri içindeki geniş, trafikte gidiş geliş yönleri ayrılmış caddedir.
Meydan: Yerleşim yerlerinde caddelerin veya büyük yolların, bulvarların birleştiği geniş alanlardır.
Cadde: Yerleşim yeri içindeki geniş ve uzunca sokaktır.
Sokak: Bir veya iki tarafına binaların sıralandığı, yayaların ve/veya araçların geçmesi için ayrılan, başı ve sonu belirli yoldur.
Küme Evler: Bir sokağa bağlanması mümkün olmayan, dağınık birden fazla binanın oluşturduğu yerleşim alanıdır.
Mezra: İdari olarak bir köye bağlı kırsal alanda olan ve birkaç evden oluşan İçişleri Bakanlığınca tescil edilmiş yerleşim alanıdır.
Mevki: Halk arasında yerleşim yerleri dışında kalan alanların tanımlanmasında kullanılan ifadedir.
Site: Genellikle bir merkezden yönetilen binalar grubudur.
Sabit Tanıtım Numarası: Mahalle, meydan, bulvar, cadde, sokak ve küme evlere karşılık gelecek şekilde, standart sayısal eşdeğer olarak verilen numaradır.

## Slide 50: Adres ve Numaralamaya İlişkin Yönetmelik
Mahalleye ad verilmesi
Her mahalleye özel bir ad verilir. Belediye sınırları içinde, aynı ad birden fazla mahalleye verilemez. Mahalle sınırları meydan, bulvar, cadde veya sokaklardan geçecek şekilde belirlenir.
Mahallelere sabit tanıtım numaralarının verilmesi
Sabit tanıtım numaraları, belediye teşkilatı bulunan yerlerde mahalleler için 1’den başlamak suretiyle son mahalleye kadar birer artırılarak verilir. Yeni mahalle kurulması durumunda yeni mahallenin sabit tanıtım numarası, daha önce verilmiş olan son tanıtım numarasını takip eden tamsayı olur. Mahallenin sadece adının değişmesi durumunda sabit tanıtım numarası değişmez. Herhangi bir mahalle için kullanılan sabit tanıtım numarası, başka bir yerleşim birimine bağlanma, birleşme, ayrılma gibi nedenler ile mahalle ortadan kalktığında iptal edilir. İptal edilen mahalleye ait sabit tanıtım numarası bir daha kullanılmaz. (4) Bir mahallenin bölünüp, birden fazla yeni mahalle kurulması durumunda, yeni kurulan mahallelerin sabit tanıtım numaraları son kullanılan mahalle sabit tanıtım numarasını takip ed

## Slide 51
Meydan, bulvar, cadde, sokak ve küme evlere ad verilmesi: Her bulvar, cadde, sokak ve küme evlere özel bir ad veya numara verilir. Meydanlara sadece ad verilir. Bir belediye sınırları içinde, aynı ad veya numara birden fazla meydan, bulvar, cadde, sokak ve küme evlere verilemez.
Meydan, bulvar, cadde, sokak ve küme evlere sabit tanıtım numarası verilmesi: Meydan, bulvar, cadde, sokak ve küme evlere, verilen ad ya da numaranın yanı sıra, ayrıca sabit tanıtım numarası verilir. Meydan, bulvar, cadde, sokak ve küme evlere sabit tanıtım numarası mahallenin, yerleşim yerinin merkezine en yakın bir ucundan başlanılarak verilir. Sabit tanıtım numaraları aynı mahalle içindeki meydan, bulvar, cadde, sokak ve küme evlerinin birbirine yakınlıkları dikkate alınarak, 1’den başlayarak ardışık olarak verilir. Eğer bir bulvar, cadde veya sokak birden fazla mahalleden geçiyorsa, sabit tanıtım numaraları her mahalle için farklı verilir.

## Slide 54
Sokak ve cadde yönü tespiti
Sokağın, cadde veya bulvarın yönü en yakın merkez esas alınarak tesbit edilir.
Ayrıca, önemli merkezler esas alınarak sokakların başlangıcı belirlenir, başlangıca göre sağ taraf çift sol taraf tek numaraları alır.

## Slide 55
Numara verilecek binalar: Numara verilmesi gereken yapılar, her çeşit resmi binalarla ev, apartman, işyeri, cami, otel, fabrika, depo ve benzeri bütün binalardır. Bir binaya numara verilmesi için ikamete mahsus olup olmadığına, kullanım şekline, yapı belgelerinin bulunup bulunmadığına bakılmaz.
Bina niteliğinde olmayan fakat içinde devamlı olarak ikamet edilen yerlere de geçici numara verilir.
Binaların sokak üzerindeki dükkan, mağaza, yazıhane ve benzeri işyerlerine bina numarası esas alınarak harfli numara verilir.“Ç, Ş, İ, Ö, Ü, Ğ, J” harfleri kullanılamaz.

## Slide 56
Bir avlu içindeki binaların numaralanmasınaların numaralandırılması Sokağa bir kapı ile açılan ve içinde müstakil binalar bulunan avlu veya bahçe içindeki binalar, sokağın hangi tarafında ise bulunduğu tarafın numaraları (tek ise tek numaralar, çift ise çift numaralar) dikkate alınarak numaralandırılır.

## Slide 57
Site içindeki binaların numaralanması: Sitenin meydan, bulvar, cadde veya sokaklardan birine açılan tek bir giriş kapısının bulunması durumunda giriş kapısına, giriş kapısının bulunduğu bulvar, cadde veya sokak üzerindeki son bina veya arsaya verilmiş olan numarayı takip eden numara verilir. Site içinde yer alan binalara giriş kapısının solundan başlayarak site giriş kapısını takiben ardışık olarak harfli birleşik numaralar verilir

## Slide 58
Sitenin meydan, bulvar, cadde veya sokaklardan birine açılan birden fazla giriş kapısının bulunması durumunda giriş kapılarına, giriş kapısının bulunduğu bulvar, cadde veya sokak üzerindeki son bina veya arsaya verilmiş olan numarayı takip eden numara verilir. Site içinde yer alan binalara, sitenin giriş kapılarından en işlek ve geniş olan yere açılan kapısının numarasını takiben, soldan başlanarak ardışık olarak harfli birleşik numaralar verilir

## Slide 59
Birden fazla sokakta kapısı bulunan binaların numaralanması: Birden fazla sokağa açılan kapıları bulunan binalara her sokaktan, bağımsız numara verilir.
Örnek: Tamer Sokaktan 24 numarayı, Serdar Sokaktan 18 numarayı alan bir binanın aktif numarası 18 olup, iç kapı numaralarıda bu numaradan verilir, diğer Tamer sokaktan aldığı 24 numara bu bina için Tamer sokaktan aldığı tahsis numarasıdır.

## Slide 60
Apartman, resmi bina, otel ve iş hanlarının iç kapılarının numaralanması: Bir evin veya apartmanın bahçe içinde yer alan ve sokakla hiçbir bağlantısı olmayan bağımsız daire niteliğinde olan yerlere, apartman daireleri gibi iç kapı numarası verilir. Bu yerlere verilen numaralar, apartman dairelerinden sonuncusuna verilen numarayı takip eder.

## Slide 61
Bir sokağın bir tarafındaki dağınık binaların numaralandırılması: Bir sokağa bağlanabilecek durumda olan dağınık binalara, sokağın sağ veya sol tarafında bulunmalarına göre, birbirini takip eden çift veya tek numaralar verilir.
Bir sokağın bir tarafında dağınık binaların bulunması durumunda aşağıdaki örnekte olduğu gibi numaralama gerçekleştirilir.

## Slide 62
Bir sokağa bağlanamayan dağınık binaların numaralandırılması: Bir sokağa bağlanmayan dağınık binaların numaralanması yine tanımlı alana en yakın bina esas alınarak yılankavi biçimde yapılır.

## Slide 63
Bir arsa veya bir bina alanına birden fazla bina yapılması: Numaralı bir alanda bina yapılacak arsa yada binadan sonra herhangi bir bina yok ise yeni yapılan binalardan ilkine daha önce arsaya tahsis edilen veya binaya verilen numara ikincisine ise ya kendisinden önceki binadan sonra gelen numara verilir. Eğer numara almış bir bina mevcut ise arsa veya bina yerine yapılan iki binadan ilkine daha önce kullanılan numara ikincisine ise kesirli numara verilir

## Slide 64
Birden fazla bağımsız bölüm içeren binalarda iç kapı numarası konut ise aşağıdaki şekilde verilir.