## Slide 1: Construction Management
Recitation-2

## Slide 2: Composite Cash Flows
Example 1:
Calculate the value of this cash flow at the end of 10th year. Annual interest rate is 10%.

## Slide 3
Example 1:
Calculate the value of this cash flow at the end of 10th year. Annual interest rate is 10%.
Solution

## Slide 4
500 ( F/P, 10%, 10 )
Solution

## Slide 5
A= 500 + 100 ( A/G, 10%, 3)
F3 = A ( F/A, 10%, 3)
= [500 + 100 ( A/G, 10%, 3 )] ( F/A, 10%, 3 )
1) Calculation of A value for the arithmetic gradient series.
2) Formula for calculation of F value when A, i and N are given.
3) Calculation of F value for the single payment
F10 = F3 (F/P, 10%, 7) F10 is the future value for F3
F10 = [500 + 100 ( A/G, 10%, 3 )] ( F/A, 10%, 3 ) ( F/P, 10%, 7 )

## Slide 6
2) Formula for calculation of F value when A, i and N are given.
F9= 700 ( F/A, 10%, 6 )
2) Calculation of F value for the single payment
F10= F9 ( F/P, 10%, 1 ) F10 is the future value of F9.
= ( F/A, 10%, 6 ) ( F/P, 10%, 1 )

## Slide 7
F + 500 ( F/P, 10%, 10 ) + [500 + 100 ( A/G, 10%, 3 )] ( F/A, 10%, 3 ) ( F/P, 10%, 7 ) - 700 ( F/A, 10%, 6 ) ( F/P, 10%, 1 ) = 0
F + 500 x 2,594 + ( 500 + 100 x 0,9366 ) x (3,310) x (1,949) - 700 x 7,716 x 1,1 = 0
F + 1.297 + 3.829,81 - 5.941,32 = 0
F = 814,51 $

## Slide 8
200
250
300
A=650
0
1
2
3
4
5
6
7
8
9
10
P=?
Example 2:
Calculate the net present value of cash flow given below. Annual interest rate is 10%.
200
50
100
A=650
0
1
2
3
4
5
6
7
8
9
10
P=?
200
200

## Slide 9
P= A1(P/A, %10, 3)+ G(P/G, %10, 3)+ A2(P/A,%10,6)*(P/F, %10, 4)
= 200*(2.4869) + 50*(2.3291) + 650*(4.3553)*(0.6830)
= 497.38 + 116.455+ 1933.54 >>>> P=2547
P=2547
First Solution
200
50
100
A=650
0
1
2
3
4
5
6
7
8
9
10
P=?
200
200

## Slide 10
P= [A1+ G*(A/G, %10,3)]*(P/A, %10, 3) + A2(P/A,%10,6)*(P/F, %10, 4)
P= [200+50(0.9366)]* 2.4869 + 650*(4.3553)*(0.6830)
= (246.83*2.4869) + 1933.54 =613.84+1933.54
P=2547
Second Solution
200
250
300
A=650
0
1
2
3
4
5
6
7
8
9
10
P=?

## Slide 11
Example 3:
The two cash flow given below are equal to each other for an interest rate of 10%. . Please calculate the X value.
0 1 2 3 4 5 6 7
0 1 2 3 4 5 6
≡
100 $
X
X
X
X
Solution
P = 100 ( P/A, 10%, 7 ) – 100 ( P/F, 10%, 2 ) = (100 x 4,8684) – (100 x 0,826) = 404,19 $
(4,8684) (0,8265) read from interest table
404,19 = X + X ( P/F, 10%, 2 ) + X ( P/F, 10%, 4 ) + X ( P/F, 10%, 6 )
404,19 = 3,074X
X = 131,49 $
100 $
100 $
100 $
100 $
100 $
0 1 2 3 4 5 6 7

## Slide 12
0
1
2
3
4
5
6
7
8
200
100
200
100
300
400
500
i=%8
i=%10
Solution 4:
Please calculate the net present value of cash flow given below.
Solution
P= F1(P/F, %8, 1)- F2(P/F, %8, 2)+(A1+G(A/G, %10, 5)*(P/A, %10, 5)*(P/F, %8, 3)
P=945,306

## Slide 13
Problem-3: With an interest rate of 8% per annum, 10000 liras was withdrawn from the bank. In the first year, a certain amount was paid, in the following years respectively 500 TL, 1500 TL, 3000 TL and 5000 TL were added to the amount paid in the first year. Find the amount of the first payment accordingly?
Solution
10.000(A/P, 8%, 5) = X + [500(P/F, 8%, 2) (A/P, 8%, 5)] + [1.500(P/F, 8%, 3) (A/P, 8%, 5)] + [3.000(P/F, 8%, 4) (A/P, 8%, 5)] + 5000(A/F, 8%, 5)
10.000 x 0,25046 = X + (500 x 0,8573 x 0,25046) + (1.500 x 0,7938 x 0,25046) + (3.000 x 0,7350 x 0,25046) + 5.000 x 0,17046
2.504,60 = X + 107,36 + 298,22 + 552,26 + 852,30
X = 2.504,60 - 1.810,14
= 694,46 TL
1- First Solution
5
4
3
2
1
P = 10.000 TL
X
X + 500
X + 1500
X + 3000
X + 5000
i = 8 %

## Slide 14
Problem-3: With an interest rate of 8% per annum, 10000 liras was withdrawn from the bank. In the first year, a certain amount was paid, in the following years respectively 500 TL, 1500 TL, 3000 TL and 5000 TL were added to the amount paid in the first year. Find the amount of the first payment accordingly?
Solution
5
4
3
2
1
P = 10.000 TL
X
500
1500
3000
5000
i = 8 %
10.000 - [500 *(P/F, 8%, 2) + 1500* (P/F, 8%, 3) + 3000* (P/F, 8%, 4) + 5000 *(P/F, 8%, 5) - X *(P/A, 8%, 5) ] = 0
10.000 - [(500* 0.8573) + (1500*0.7938) + (3000*0.7350) + (5000* 0.6806) – (3.9927 X ) ] = 0
10.000 - 428.65 + 1190.7 + 2205 + 3403 - 3.9927 X = 0
3.9927 X = 2772,65
X = 694,46 TL
Second Solution
5
4
3
2
1
P = 10.000 TL
X
X + 500
X + 1500
X + 3000
X + 5000
i = 8 %
X
X
X
X

## Slide 15
Example 6:
A construction company compares two alternatives. The first alternative is an automatic feeding machine, the other is a manual feeding machine.
The initial cost of the first alternative, which is thought to have a 10-year economic life, is 23000 TL and the estimated salvage value is 4000 TL. Operation cost is 12 TL per hour. The expected production amount per hour is 8 tons. Annual maintenance and operation costs are considered to be 3500 TL.
The second machine, which is considered as an alternative, has an initial cost of 8000 TL and no salvage value. Its economic life is estimated to be 5 years. In order to make this machine 6 tons per hour, three workers must be employed for 8 TL per hour. Annual maintenance and operation costs are estimated to be 1500 TL.
Since the whole project is estimated to yield 10%, how many tons of production should be produced per year so that an automatic machine can be selected?
-----------------------------------------------------------------------------------------------------------------------------------------------------
X represents the annual production
Annual variable cost for alternative 1= $12/hour* 1hour/8ton* x ton/year
D1= 1.5x
ENH1= - 23,000(A/P,10%,10) + 4000(A/F, 10%,10) - 3500 - 1.5x
ENH1= -6992-1.5x
Annual variable cost for alternative 2= $8/hour*3*1hour/6ton* x ton/year
D2= 4x
ENH2= - 8000(A/P,10%,5) - 1500 - 4x
ENH2 = -3610-4x
ENH1= ENH2
-6992-1.5x = -3610-4x
x= 1353 ton/yıl
If annual production exceed the 1353 tons, automatic feeding machine should be acquired.

## Slide 16: Solution 7:
Activity | Predecessor | Normal Duration | Activity Cost
A, B, C | - | 4 | 2500
D, E | C, B | 5 | 3500
F | A | 2 | 750
G | F, E | 7 | 450
H | D, G | 8 | 1000
It is assumed that each activity will be completed without any delay and Cost of each activity will be paid right after its completion.
A client thinks to deposit all money required to complete this project into a bank with an interest rate of 2%, in order pay less amount of money. How much money this client should deposit to be able to cover all the expenses of the project.

## Slide 17: Solution
B
4
A
4
C
4
F
2
D
5
G
7
H
8
E
5
0
0
7
4
9
9
16
16
24
24
4
4
4
4

## Slide 18
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
7500
750
7000
450
1000
P=?